## Slide 1
NumaConnect
Technology
Steffen Persvold, Chief Architect
OPM Meeting, 11.-12. March 2015

## Slide 2: Technology Background
Dolphin’s Low
Latency Clustering HW
Dolphin’s
Cache Chip
Convex Exemplar (Acquired by HP)
  First implementation of the ccNUMA architecture from Dolphin in 1994
Data General Aviion (Acquired by EMC)
  Designed in 1996, deliveries from 1997 - 2002
  Dolphin chipset with 3 generations of Intel processor/memory buses
I/O Attached Products for Clustering OEMs
  Sun Microsystems (SunCluster)
  Siemens RM600 Server (IO Expansion)
  Siemens Medical (3D CT)
  Philips Medical (3D Ultra Sound)
  Dassault/Thales Rafale
HPC Clusters (WulfKit w. Scali)
  First Low Latency Cluster Interconnect
Convex Exemplar Supercomputer

## Slide 3: NumaChip-1
IBM Microelectronics ASIC
FCPBGA1023, 33mm x 33mm, 1mm ball pitch, 4-2-4 package
IBM cu-11 Technology
~ 2 million gates
Chip Size 9x11mm

## Slide 4: NumaConnect-1 Card

## Slide 5: SMP - Symmetrical
CPU
Shared Memory
CPU
CPU
I/O
BUS
SMP used to mean “Symmetrical Multi Processor”

## Slide 6: SMP – Symmetrical, but…
Caches complicate - Cache Coherency (CC) required
Caches
CPUs
Caches
Shared Memory
Caches
CPUs
Caches
Caches
CPUs
Caches
I/O
BUS
zzz

## Slide 7: NUMA – Non Uniform Memory Access
Point-to-point Links
Caches
CPUs
I/O
Memory
Caches
CPUs
Memory
Caches
CPUs
Memory
Caches
Caches
Caches
zzzzzz
Access to memory controlled by another CPU is slower - Memory Accesses are Non Uniform (NUMA)

## Slide 8: SMP - Shared MP - CC-NUMA
Caches
CPUs
I/O
Memory
Caches
CPUs
Memory
Caches
CPUs
Memory
  Caches
Caches
Caches
Foo
Foo
Foo
zzzzzzzzz
Non-Uniform Access Shared Memory with Cache Coherence

## Slide 9: SMP - Shared MP - CC-NUMA
Caches
CPUs
I/O
Memory
Caches
CPUs
Memory
Caches
CPUs
Memory
  Caches
Caches
Caches
Foo
Foo
Foo
Foo
Foo
zzzzzzzzzzz
Non-Uniform Access Shared Memory with Cache Coherence

## Slide 10: SMP - Shared MP - CC-NUMA
Non-Uniform Access Shared Memory with Cache Coherence
Caches
CPUs
I/O
Memory
Caches
CPUs
Memory
Caches
CPUs
Memory
  Caches
Caches
Caches
Foo
Fool
Fool
Foo
Zzzzzzz
Zzzzzzz!

## Slide 11: Numascale System Architecture
Shared Everything - One Single Operating System Image
Caches
CPUs
I/O
Memory
Caches
Caches
CPUs
I/O
Memory
Caches
Caches
CPUs
I/O
Memory
Caches
I/O
Memory
Caches
CPUs
Caches
NumaConnect Fabric - On-Chip Distributed Switching
NumaChip
Numa Cache
NumaChip
Numa Cache
Numa Cache
NumaChip
Numa Cache
NumaChip

## Slide 12: NumaConnect™ Node Configuration
NumaChip
Memory
Numa
Cache+Tags
Multi-Core
CPU
I/O Bridge
Memory
Memory
Memory
Memory
Multi-Core
CPU
Memory
Memory
Memory
Memory
Coherent HyperTransport
6 x4 SERDES links

## Slide 13: NumaConnect™ System Architecture
3-D Torus
2-D Torus
6 external links - flexible system configurations in multi-dimensional topologies
Multi-CPU Node
NumaChip
Memory
Numa
Cache
Multi-Core
CPU
I/O Bridge
Memory
Memory
Memory
Memory
Multi-Core
CPU
Memory
Memory
Memory
Memory

## Slide 14: NumaChip-1 Block Diagram
SPI Init Module
SDRAM Cache
SDRAM Tags
HyperTransport
SPI
XA
XB
YB
YA
ZA
ZB
LC Config Data
Microcode
SM
CSR
ccHT Cave
H2S
SCC
Crossbar switch, LCs, SERDES

## Slide 15: 2-D Dataflow
Request
Response
CPUs
Caches
NumaChip
Memory
Memory
Memory
Memory
CPUs
Caches
Memory
Memory
Memory
Memory
NumaChip
CPUs
Caches
Memory
Memory
Memory
Memory
NumaChip

## Slide 16: The Memory Hierarchy
Chart: Latencies in the Memory Hierarchy
| L1 | L2 | L3 | Local Memory | Neighbor Socket | NumaCache | Remote Memory | SSD | Disk
 | 1.251 | 6.421 | 16.732 | 75 | 125 | 308 | 1087 | 100000 | 50000000

## Slide 17: LMbench - Chart
NumaCache(L4)
RemoteMemory
CPU Caches
L2
L3
L1
Chart: Latency - LMBench
| 0,00049 | 0,00098 | 0,00195 | 0,00293 | 0,00391 | 0,00586 | 0,00781 | 0,01172 | 0,01562 | 0,02344 | 0,03125 | 0,04688 | 0,0625 | 0,09375 | 0,125 | 0,1875 | 0,25 | 0,375 | 0,5 | 0,75 | 1 | 1,5 | 2 | 3 | 4 | 6 | 8 | 12 | 16 | 24 | 32 | 48 | 64 | 96 | 128 | 192 | 256 | 384 | 512 | 768 | 1024 | 1536 | 2048 | 3072 | 4096 | 6144
Untitled 2 | 1.251 | 1.252 | 1.252 | 1.252 | 1.252 | 1.252 | 1.252 | 1.252 | 1.253 | 1.253 | 1.264 | 1.254 | 1.254 | 6.413 | 6.421 | 6.413 | 6.474 | 6.425 | 6.427 | 16.213 | 16.732 | 16.748 | 16.743 | 17.124 | 17.054 | 147.125 | 223.371 | 287.01 | 294.956 | 302.961 | 305.637 | 306.743 | 308.61 | 303.582 | 304.297 | 303.062 | 302.749 | 304.299 | 302.936 | 303.697 | 303.3 | 302.221 | 304.582 | 628.583 | 1087.576 | 1026.939
1,251
6,421
16,732
308
1087

## Slide 18: Principal Operation – L1 Cache Hit
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
To/From Other nodes
in the same dimension
L1 Cache HIT

## Slide 19: Principal Operation – L2 Cache Hit
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
To/From Other nodes
in the same dimension
L2 Cache HIT

## Slide 20: Principal Operation – L3 Cache Hit
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
To/From Other nodes
in the same dimension
L3 Cache HIT

## Slide 21: Principal Operation – Local Memory
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
To/From Other nodes
in the same dimension
Local Memory Access, HT Probe for Shared Data

## Slide 22: Principal Operation – NumaCache Hit
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
To/From Other nodes
in the same dimension
Remote Memory Access, Remote Cache Hit

## Slide 23: Principal Operation – Remote Memory
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
Memory
L3 Cache
Mem. Ctrl.
HT Interface
CPU Cores
L1&L2 Caches
NumaChip
NumaCache
To/From Other nodes
in the same dimension
Remote Memory Access, Remote Cache Miss

## Slide 24: NumaChip Features
Converts between snoop-based (broadcast) and directory based coherency protocols
Write-back to NumaCache
Coherent and Non-Coherent Memory Transactions
Distributed Coherent Memory Controller
Pipelined Memory Access (16 Outstanding Transactions)
NumaCache size up to 8GBytes/Node
  Current boards support up to 4Gbytes NumaCache

## Slide 25: Scale-up Capacity
Single System Image or Multiple Partitions
Limits
  256 TeraBytes Physical Address Space
  4096 Nodes
  196 608 cores
Largest and Most Cost Effective Coherent Shared Memory
Cache Line (64Bytes) Coherency

## Slide 26: NumaConnect in Supermicro 1042

## Slide 27: Cabling Example

## Slide 28: 5 184 Cores – 20.7 TBytes
108 nodes
6 x 6 x 3 Torus
5 184 CPU cores
58 TFlops
20.7 TBytes Shared Memory
Single Image OS

## Slide 29
OPM ”cpchop” scaling
Steffen Persvold, Chief Architect
OPM Meeting, 11.-12. March 2015

## Slide 30: What is scaling ?
In High Performance Computing there are two common notions of scaling:
Strong scaling
  How the solution time varies with the number of processors for a fixed total problem size.
    \eta_p = t1 / ( N * tN ) * 100%
Weak scaling
  How the solution time varies with the number of processors for a fixed problem size per processor.
    \eta_p = ( t1 / tN ) * 100%

## Slide 31: OPM – “cpchop” What was done ?
3 weeks to enable “cpchop” scalability
Initial state (Jan ‘14):
  No scaling beyond 4 threads on a single server node
A few changes after code analysis enabled scalability
  Removed #pragma omp critical sections from opm-porsol (needed fixes to dune-istl/dune-common) (Arne Morten)
  Removed excessive verbose printouts (not so much for scaling but for “cleaner” multithreaded output).
  Made sure thread context was allocated locally per thread.
  Created local copies of the parsed input.
  Dune::Timer class changed to use clock_gettime(CLOCK_MONOTONIC, &now) instead of std::clock() and getrusage() avoiding kernel spinlock calls
    When building UMFPACK use –DNO_TIMING in the configuration or modify the code to use calls without spinlocks
  Reduced excessive use of malloc/free by setting environment variables MALLOC_TRIM_THREASHOLD_=-1, MALLOC_MMAP_MAX_=0, MALLOC_TOP_PAD_=536870912 (500MB)

## Slide 32: OPM – “cpchop” Making local object copies
diff --git a/examples/cpchop.cpp b/examples/cpchop.cpp
index 212ac53..da52c6a 100644
--- a/examples/cpchop.cpp
+++ b/examples/cpchop.cpp
@@ -617,7 +617,16 @@ try
#ifdef HAVE_OPENMP
threads = omp_get_max_threads();
#endif
- std::vector<ChopThreadContext> ctx(threads);
+ std::vector<ChopThreadContext*> ctx(threads);
+
+#pragma omp parallel for schedule(static)
+ for (int i=0;i<threads;++i) {
+ int thread = 0;
+#ifdef HAVE_OPENMP
+ thread = omp_get_thread_num();
+#endif
+ ctx[thread] = new ChopThreadContext();
+ }
// draw the random numbers up front to ensure consistency with or without threads
std::vector<int> ris(settings.subsamples);

## Slide 33: OPM – “cpchop” Distribute input
@@ -638,6 +643,42 @@ try
rzs[j] = rz();
}
+#ifdef HAVE_HWLOC
+ Dune::Timer watch1;
+ Numa::Topology numatopology;
+
+ // Create a local copy of the CornerPointChopper object, one per numa board used
+ int boards = numatopology.num_boards();
+
+ std::vector<Opm::CornerPointChopper*> ch_local(boards);
+ std::atomic<bool> have_ch_local[boards];
+ for (int i=0;i<boards;++i) {
+ have_ch_local[i] = false;
+ }
+
+ // Assign the master instance into our pointer vector
+ {
+ int board = numatopology.get_current_board();
+ ch_local[board] = &ch;
+ have_ch_local[board] = true;
+ }

## Slide 34: OPM – “cpchop” Distribute input cont’d
+
+ std::cout << "Distributing input to boards" << std::endl;
+ int distributed = 0;
+
+#pragma omp parallel for schedule(static) reduction(+:distributed)
+ for (int i = 0; i < threads; ++i) {
+ int board = numatopology.get_current_board();
+
+ if (!have_ch_local[board].exchange(true)) {
+ ch_local[board] = new Opm::CornerPointChopper(ch);
+ distributed++;
+ }
+ }
+
+ std::cout << "Distribution to " << distributed << " boards took " << watch1.elapsed() << " seconds" << std::endl;
+#endif // HAVE_HWLOC
+
double init_elapsed = watch.elapsed();
watch.reset();

## Slide 35: OPM – “cpchop” scaling
Chart: 
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 48.0 | 64.0 | 80.0 | 96.0 | 112.0 | 128.0
init_T | 32.0727 | 31.3961 | 31.7657 | 32.7903 | 32.1619 | 39.9858 | 46.7636 | 54.8208 | 61.7843 | 66.9054 | 73.1943 | 83.2206
solve_T | 580.472 | 763.323 | 868.447 | 850.576 | 852.74 | 844.772 | 845.539 | 850.081 | 851.462 | 854.857 | 858.385 | 850.478
\eta_p | 1 | 0.77077 | 0.68044 | 0.69342 | 0.69222 | 0.69233 | 0.68648 | 0.67692 | 0.67073 | 0.66454 | 0.65753 | 0.65604
node_\eta_p | 1 | 1.0002 | 0.99171 | 0.9779 | 0.96896 | 0.96001 | 0.94989 | 0.94774